## Slide 1
Abdul Rafey | 20042868 | STM32F407 Hardware-Adaptive TinyML
Hardware-Adaptive TinyML Inference on STM32F407
Applied Research Project Presentation / Artefact Demonstration
Abdul Rafey | Student ID: 20042868 | MSc in Computing | Dublin Business School | 2026
STM32F407
X-CUBE-AI
Real Board Telemetry
1

## Slide 2
Abdul Rafey | 20042868 | STM32F407 Hardware-Adaptive TinyML
Problem Context
Static TinyML deployment does not react to changing microcontroller hardware state.
Industry / technical problem
TinyML models are often deployed as fixed firmware pipelines.
Microcontrollers operate under changing temperature, voltage and CPU-load conditions.
A compiled model may invoke successfully but still produce unusable output if deployment is wrong.
Observed project problem
Rule engine was working, but early AI output was zero.
TensorFlow Lite Micro returned Invoke=0, but output probabilities were S=0.000, P=0.000, M=0.000.
This showed the need for output validation, not only build success.
Hardware state
Temp / Vcc / CPU
Static model
Fixed inference path
Runtime risk
Latency / stability issue
Need
Adaptive decision
3

## Slide 3
Abdul Rafey | 20042868 | STM32F407 Hardware-Adaptive TinyML
Aim and Research Questions
The aim was to build and evaluate a hardware-adaptive TinyML inference artefact.
Project aim
Design, implement and evaluate a hardware-level adaptive TinyML framework on STM32F407.
Use real board telemetry to select a suitable inference mode during runtime.
Core research questions
How can STM32F407 telemetry support dynamic mode selection?
How does AI + rule fallback improve stability?
What implementation changes were needed to make the model run reliably?
Hypothesis summary
Temperature and CPU-load telemetry can support stable inference-mode selection.
A confidence-gated model with fallback rules can reduce uncertain switching.
Correct STM32 toolchain configuration is necessary for reliable Cortex-M4 inference.
4

## Slide 4
Abdul Rafey | 20042868 | STM32F407 Hardware-Adaptive TinyML
Artefact Overview
The artefact is a complete STM32F407 hardware-adaptive TinyML firmware system.
Hardware profiler
Temp / Vcc / CPU
AI model
Temp + CPU input
Rule engine
Safety fallback
Fusion logic
75% confidence gate
UART log
Decision evidence
Output modes
STANDARD_INT8
PRUNED_VARIANT
MIXED_PRECISION
Final decision fields
Rule
AI
Decided
Src = AI or RULE
Submission evidence
GitHub repository
Dataset copy
Model files
UART screenshots
5

## Slide 5
Abdul Rafey | 20042868 | STM32F407 Hardware-Adaptive TinyML
Tools and Technologies
The artefact combines embedded firmware, model training, and STM32-native AI deployment.
Hardware and firmware
STM32F407 / STM32F407VGTX
ARM Cortex-M4 with FPU
STM32CubeIDE
STM32CubeMX
STM32 HAL drivers
UART / PuTTY logging
Machine learning stack
Python / Google Colab
TensorFlow 2.20
Keras model
TFLite export
Two inputs: Temp + CPU
Three-class softmax output
Deployment stack
X-CUBE-AI 10.2.0
Generated C inference code
model_manager_xcubeai.c
hard floating-point ABI
Rule + AI fusion logic
GitHub artefact repository
6

## Slide 6
Abdul Rafey | 20042868 | STM32F407 Hardware-Adaptive TinyML
Data Collection and Dataset
The model was trained on real STM32F407 board telemetry, not a public HAR dataset.
1,395
Telemetry rows collected
3
Runtime phases: cold boot, stress, normal
2
Final model inputs: temperature + CPU
3
Mode classes predicted
Logged variables
Temperature
Vcc / supply voltage
CPU load estimate
Phase and stress state
Rule labels and UART debug output
Feature decision
Voltage was collected and analysed.
Vcc variation was too small in the available setup.
Final model therefore used temperature and CPU load only.
7

## Slide 7
Abdul Rafey | 20042868 | STM32F407 Hardware-Adaptive TinyML
Model Training Pipeline
A small float32 classifier was trained and exported for STM32 deployment.
CSV data
data_training.csv
Feature analysis
Drop Vcc
Normalisation
Z-score constants
Training
Dense 2→16→3
Export
model.keras + model.tflite
Model architecture
Input shape: (2,)
Dense hidden layer: 16 ReLU
Output layer: 3 Softmax
Training settings
80/20 stratified split
Adam optimizer
Sparse categorical crossentropy
EarlyStopping patience = 10
Training result
Held-out accuracy: 83.2%
Inputs: temperature + CPU
Classes: Standard / Pruned / Mixed
8

## Slide 8
Abdul Rafey | 20042868 | STM32F407 Hardware-Adaptive TinyML
Runtime System Architecture
The final runtime links hardware profiling, X-CUBE-AI inference, rule fallback and UART evidence.
Hardware Profiler
Reads temp, Vcc, CPU
Normalisation
Uses training constants
X-CUBE-AI Model
Softmax S/P/M
Rule Engine
Threshold fallback
Decision Fusion
AI if conf ≥ 0.75
UART Output
Rule / AI / Decided / Src
Final runtime behaviour
Each loop samples board state, runs the model, calculates confidence, applies fallback logic, then prints the final decision over UART.
Validation rule
The artefact is considered working only when UART shows non-zero probabilities, confidence, Rule, AI, Decided and Src fields.
9

## Slide 9
Abdul Rafey | 20042868 | STM32F407 Hardware-Adaptive TinyML
Decision Fusion Logic
The final decision uses AI confidence first, then rule fallback when confidence is low.
AI Output
S, P, M probabilities
Confidence
≥ 0.75?
Use AI
Src=AI
Use Rule
Src=RULE
Final Decided
Mode
Rule thresholds
MIXED_PRECISION: temp > 66.8°C or CPU > 64%
STANDARD_INT8: CPU < 48–50%
PRUNED_VARIANT: middle region
AI output mapping
Output 0 = STANDARD_INT8
Output 1 = PRUNED_VARIANT
Output 2 = MIXED_PRECISION
Why fallback matters
Prevents uncertain AI output from causing unstable switching near class boundaries.
10

## Slide 10
Abdul Rafey | 20042868 | STM32F407 Hardware-Adaptive TinyML
Implementation Issues and Fixes
The final working path was achieved after debugging the embedded deployment layer.
Problem encountered
TensorFlow Lite Micro integration was attempted first.
Invoke appeared successful but output tensor values were zero.
Pointer/output handling created repeated debugging issues.
Technical fixes
Migrated final deployment to X-CUBE-AI 10.2.0.
Removed unnecessary microlite library dependency.
Generated STM32-compatible C inference files.
Kept same normalisation constants in firmware.
Project property fix
STM32CubeIDE floating-point ABI changed from softfp to hard.
This supports Cortex-M4 FPU usage for float32 inference.
Final UART output confirmed valid probabilities.
11

## Slide 11
Abdul Rafey | 20042868 | STM32F407 Hardware-Adaptive TinyML
Results and Runtime Evidence
The final deployment is validated by actual Putty/UART output from the STM32F407 board.
83.2%
Held-out test accuracy
0.75
Confidence threshold
3
Output classes
AI / RULE
Decision source
12
Actual final UART output: each row prints Temperature, Voltage, CPU load, AI prediction, Rule decision, Decided mode, and Src (AI or RULE).
STANDARD region
CPU 44–48% → AI=STANDARD_INT8
Confidence up to 1.000
Source mostly AI
PRUNED region
CPU around 51–55% → PRUNED_VARIANT
AI and Rule agree
Stable middle mode
Fallback proof
AI=MIXED at 0.581
Rule chooses PRUNED
Src=RULE

## Slide 12
Abdul Rafey | 20042868 | STM32F407 Hardware-Adaptive TinyML
Limitations and Future Work
The prototype works, but future versions can expand the hardware evaluation and runtime switching.
Current limitations
Dataset comes from one STM32F407 board and one firmware configuration.
Voltage variation was too small in available data, so Vcc was not used as a final AI input.
Energy results require stronger measurement with external current-sensing hardware.
Future work
Implement real switching between multiple compiled X-CUBE-AI networks.
Collect a larger dataset under controlled thermal and voltage sweeps.
Add hysteresis/smoothing around decision boundaries.
Test portability on other STM32 Cortex-M boards.
Practical implication
The project provides a foundation for hardware-aware TinyML systems where embedded inference decisions are influenced by live board state rather than only by static offline optimisation.
14

## Slide 13
Abdul Rafey | 20042868 | STM32F407 Hardware-Adaptive TinyML
Conclusion
The project converted hardware-aware TinyML from an idea into a working STM32F407 artefact.
Main contribution
Real STM32F407 board telemetry dataset
Hardware-adaptive mode-selection logic
X-CUBE-AI deployed AI model
Rule fallback for low-confidence regions
Final evidence
Model output no longer zero
Softmax probabilities available
Confidence and source fields printed
Artefact can be demonstrated through UART
Submission package
Report PDF
Presentation PPTX
Artefact folder
GitHub repository link in report appendix
Thank you — Questions?
15